## Slide 1: Lecture 02: More on Memory and I/O Modules

## Slide 2: Reference Book:
William Stallings Computer Organization and Architecture
  Chapter 5 Internal Memory
微型计算机原理与接口技术（第四版）
  第五章 存储器

## Slide 3: Characteristics of Memory
Location
Capacity
Unit of transfer
Access method
Performance
Physical type
Organisation

## Slide 4: Location
CPU
  registers
Internal
  Cache, main memory
External
  Disk, tape, DVD

## Slide 5: Capacity
Word size
  The natural unit of organization
Number of words
E.g., 2M 8-bit, 16M 1-bit
  Same capacity but different organization

## Slide 6: Unit of Transfer
Internal Memory
  Usually a word, governed by data bus width
External Memory
  Usually a block which is much larger than a word

## Slide 7: Addressable unit
Smallest location which can be uniquely addressed
Normally a Byte for internal memory
Cluster on disks

## Slide 8: Access Methods (1)
Sequential 串行访问
  Start at the beginning and read through in order
  Access time depends on location of data and previous location
  e.g. tape
Direct 直接访问
  Individual blocks have unique address
  Access is by jumping to vicinity plus sequential search
  Access time depends on location and previous location
  e.g. disk

## Slide 9: Access Methods (2)
Random 随机访问
  Individual addresses identify locations exactly
  Access time is independent of location or previous access
  e.g. RAM, ROM
Associative 关联访问
  Data is located based on a portion of its contents rather than its address
  Access time is independent of location or previous access
  e.g. cache

## Slide 10: Performance
Access time
  Time between presenting the address and getting the valid data
Memory Cycle time
  Time may be required for the memory to “recover” before next access
  Cycle time is access + recovery
Transfer Rate
  Rate at which data can be moved

## Slide 11: Physical Types
Semiconductor
  RAM
Magnetic
  Disk & Tape
Optical
  CD & DVD
Others
  Bubble
  Hologram

## Slide 12: Semiconductor Memory
The basic element of a semiconductor memory is the memory cell
  exhibit two stable states, representing binary 1 and 0
  capable of being written into to set the state
  capable of being read from to sense the state
RAM (Random Access Memory)
  Misnamed as all semiconductor memory is random access
ROM (Read-Only Memory)

## Slide 13: Random Access Memory (RAM)
Read/Write
Volatile
  must be provided with a constant power supply
Temporary storage
  When the power is gone, data are lost
Static or dynamic
  SRAM or DRAM

## Slide 14: Dynamic RAM (DRAM)
Bits stored as charge in capacitors
Charges leak
Need refreshing even when powered
Simpler construction
Smaller per bit
Less expensive
Need refresh circuits
Slower
For the user of main memory

## Slide 15: Static RAM (SRAM)
Bits stored as on/off switches
No charges to leak
No refreshing needed when powered
More complex construction
Larger per bit
More expensive
Does not need refresh circuits
Faster
For the use of cache
traditional flip-flop logic-gate configurations

## Slide 16: Read Only Memory (ROM)
Permanent storage
Nonvolatile
  Needs no power
Normal applications of ROM
  Library subroutines
  Systems programs (BIOS)
  Function tables

## Slide 17: Types of ROM
Written during manufacture
  Very expensive for small runs
Programmable (once)
  PROM
  Needs special equipment to program
Read “mostly”
  Erasable Programmable (EPROM)
    Erased by Ultraviolet radiation
  Electrically Erasable (EEPROM)
    Takes much longer to write than read
  Flash memory
    Erase whole memory electrically

## Slide 18: Memory Hierarchy 存储器层级结构
Registers
  In CPU
Internal or Main memory
  May include one or more levels of cache
  “RAM”
External memory
  Backing store

## Slide 19: Hierarchy List
Registers
L1 Cache
L2 Cache
Main memory
Disk cache
Disk
Optical
Tape

## Slide 20: So you want fast?
It is possible to build a computer which uses only static RAM (cache)
  e.g., computers with NVM
This would be very fast
This would need no cache
This would cost a very large amount of money
Memory hierarchy is trade-offs among speed, capacity, and cost

## Slide 21: Chip Organisation
Physical arrangement of bits into words
  Note that this “word” is the chip word not the system word

## Slide 22: Organisation in detail
A 16Mbit chip can be organised as 1M of 16-bit words
A 16Mbit chip can be organised as a 2048 x 2048 x 4bit array
  Reduces number of address pins
    Multiplex row address and column address
    11 pins to address (211=2048)
    Adding one more pin doubles range of values so x4 capacity

## Slide 23: Typical 16 Mb DRAM (4M x 4)

## Slide 24: Chip Packaging

## Slide 25: Module Organisation
To organize a memory module：
If the module needs bigger unit of transfer than that of given memory chips, bit extension, 位扩展
Every chip has the same address space
A memory module consisting of 256K 8-bit words, using 8 256K1-bit chips

## Slide 26: Bit Extension Example
You have 256K1-bit RAM chips. How can you build a memory module of 256K32-bit and how to connect this module with a computer system?
A17-0
A17-0
What is the addressable unit? What is the addressing scheme used in this example?

## Slide 27: Module Organisation (2)
To organize a memory module：
If the module needs larger number of words than that of given memory chips, word extension, 字扩展
Chips in different group has different address range
A memory consisting of 1M8-bit words, having four groups of 256K1-bit chips

## Slide 28: Word Extension Example
You have 256K8-bit RAM chips. How can you build a memory module of 2M8-bit and how to connect this module with a computer system?

## Slide 29: Word and Bit Extension Example
Now you have 256K8-bit RAM chips. How can you build a memory module of 2M32-bit and how to connect this module with a computer system?
What if the addressable unit is byte?
A17-0
A20-18
A20-0

## Slide 30: Reference Book:
William Stallings Computer Organization and Architecture
  Chapter 7 Input/Output
微型计算机原理与接口技术（第四版）
  第六章 I/O接口和总线

## Slide 31: Input/Output Problems
Wide variety of peripherals（外设）
  Different operation logic
  -> impractical for CPU to control all kinds of devices
  Speak different "languages"
    Delivering different amounts of data, e.g., serial/parallel
    At different speeds
    In different formats, e.g., analog/digital
  -> impractical for CPU to understand
  Slower than CPU and RAM
  -> impractical to directly connect devices with high-speed system bus
We need I/O modules (ports)!

## Slide 32: Input/Output Module
Interface to the CPU and Memory
Interface to one or more peripherals
It's like a bridge, an interpreter, a buffer, and …

## Slide 33: External Devices
Human readable
  Screen, printer, keyboard
Machine readable
  Monitoring and control
Communication
  Modem
  Network Interface Card (NIC)

## Slide 34: I/O Module Function
Control & Timing
CPU Communication
Device Communication
Data Buffering
Error Detection

## Slide 35: I/O Steps
For example, the control of the transfer of data from an external device to the processor
  CPU checks I/O module for device status
  I/O module returns the device status
  If the device is ready, CPU requests data transfer by means of a command to the I/O module
  I/O module gets a unit of data from device
  I/O module transfers the data to CPU

## Slide 36: I/O Module Diagram
Data Register
Status/Control Register
External
Device
Interface
Logic
External
Device
Interface
Logic
Input
Output
Logic
Data
Lines
Address
Lines
control
Lines
Data
Status
Control
Data
Status
Control
Interface to Systems Bus
Interface to External Device

## Slide 37: I/O Module Design Decisions
Hide or reveal device properties to CPU
Support multiple or single device
Control device functions or leave for CPU

## Slide 38: Input Output Techniques
Programmed I/O, 程序控制I/O
Interrupt driven I/O, 中断驱动I/O
Direct Memory Access (DMA), 直接存储器访问

## Slide 39: Programmed I/O
CPU executes a program that gives it direct control of the I/O operation
  Sensing device status
  Read/write commands to the I/O module
  Transferring data
CPU waits for I/O module to complete operation

## Slide 40: Programmed I/O - detail
CPU requests I/O operation
I/O module performs operation
I/O module sets status bits
CPU checks status bits periodically
I/O module does not inform CPU directly
I/O module does not interrupt CPU
CPU may wait or come back later (for example, with the help of time-sharing OS)

## Slide 41: I/O Commands
CPU issues address
  Identifies module (& device if >1 per module)
CPU issues command
  Control - telling module what to do
    e.g. spin up disk
  Test - check status
    e.g. power? Error?
  Read/Write
    Module transfers data via buffer from/to device

## Slide 42: Addressing I/O Devices
Under programmed I/O, data transfer is very like memory access (from CPU viewpoint)
Each device is given a unique identifier
CPU commands contain the identifier (address) of the corresponding module (and device)

## Slide 43: Addressing Schemes Revisited
Memory mapped I/O
  Devices and memory share an address space
  I/O looks just like memory read/write
  No special commands for I/O
    Large selection of memory access commands available
Isolated I/O
  Separate address spaces
  Need I/O or memory select lines
  Special commands for I/O
    Limited set

## Slide 44: Problem with Programmed I/O?
Simple, but if CPU is faster,
it is a huge waste of CPU time

## Slide 45: Interrupt Driven I/O
Overcomes CPU waiting
No repeated CPU checking of device
I/O module interrupts when ready

## Slide 46: Interrupt Driven I/O Basic Operation
CPU requests I/O operation
I/O module performs operation whilst CPU does other work
I/O module informs CPU when something comes up by interrupting CPU
CPU deals with this event

## Slide 47: CPU Viewpoint
Issue read command
Do other work
Check for interrupt at the end of each instruction cycle
If interrupted:-
  Save context (registers)
  Process interrupt
    Fetch data & store
  Recover from the saved context

## Slide 48: Handling an Interrupt: from a Protocol Perspective
A program called interrupt handler
Draw a protocol:
Which parties?
Interactions?
What’s interrupt?
New event needs CPU to handle first but CPU needs to go back to previous work after that
Notes: How can the CPU know which device is generating the interrupt? What is the new PC value?

## Slide 49: Design Issues
How can CPU know which module is issuing the interrupt?
  when there are multiple devices connected to the system
How to locate the corresponding handler program when interrupted?
How do you deal with multiple interrupts?
  Possible for more than one devices to issue an interrupt simultaneously or in a row

## Slide 50: Identifying Interrupting Module (1)
Connect a dedicated line for each module
  Limits the number of devices
Software poll
  All devices share one common Interrupt Request line to interrupt CPU
  Once get an interrupt, CPU asks each module in turn
  CPU clears the interrupt request status of the module responsible

## Slide 51: Identifying Interrupting Module (2)
Daisy Chain or Hardware poll
  All devices share one common Interrupt Request line to interrupt CPU
  Interrupt Acknowledge signal is sent down a chain
Bus Master
  Module must claim the bus before it can raise interrupt
  e.g. PCI & SCSI
Interrupt controller
  8259

## Slide 52: Localizing Handler Programs
Using a general handler program
  CPU enters this handler every time it gets interrupted
  looks for the module responsible and gets the address of the corresponding handler program
Using interrupt vectors
  instead of using fixed locations, a handler program can be stored anywhere in memory
  a pointer is used to link to the handler program
  the address of the pointer is fixed and known to CPU
  such pointers are interrupt vectors
  Pros and cons?

## Slide 53: Dealing with Multiple Interrupts
  Set priorities for interrupts
  i.e., high-priority interrupts get served first
  Given a interrupt identification scheme, how to set priorities?
    Software and hardware polling, bus mastering
  Nesting of interrupts
    i.e., high-priority interrupts can further interrupt low-priority interrupts

## Slide 54: Problem with Programmed and Interrupt-driven I/O?
They both need the involvement of CPU.

## Slide 55: Direct Memory Access
Interrupt driven and programmed I/O require active CPU intervention
  Transfer rate is limited
  CPU is tied up
DMA is the answer

## Slide 56: DMA Function
Additional Module (hardware) on bus
DMA controller takes over from CPU for I/O

## Slide 57: DMA Operation
CPU tells DMA controller:-
  Read/Write
  Device address
  Starting address of memory block for data
  Amount of data to be transferred
CPU carries on with other work
DMA controller deals with transfer
DMA controller sends interrupt when finished

## Slide 58: DMA Transfer Cycle Stealing
In an instruction cycle, the processor may be suspended due to DMA operation
  CPU suspended just before it accesses bus
  DMA controller takes over bus for a cycle
  Transfer of one word of data
  Not an interrupt: CPU does not switch context
  Slows down CPU but not as much as CPU doing transfer

## Slide 59: DMA Configurations (1)
Single Bus, Detached DMA controller
Each transfer uses bus twice
  e.g., I/O to DMA then DMA to memory
For one transfer, CPU is suspended twice
CPU
DMA
Controller
I/O
Device
I/O
Device
Main
Memory

## Slide 60: DMA Configurations (2)
Single Bus, Integrated DMA controller
Controller may support >1 device
Each transfer uses bus once
  DMA to memory
For one transfer, CPU is suspended once
CPU
DMA
Controller
I/O
Device
I/O
Device
Main
Memory
DMA
Controller
I/O
Device

## Slide 61: DMA Configurations (3)
Separate I/O Bus
Bus supports all DMA enabled devices
Each transfer uses bus once
  DMA to memory
For one transfer, CPU is suspended once
CPU
DMA
Controller
I/O
Device
I/O
Device
Main
Memory
I/O
Device
I/O
Device

## Slide 62: Which way is the best?
Simplicity
Performance

## Slide 63: Assignment Two
Go Jbox/Canvas site and download the Assignment Two
  https://oc.sjtu.edu.cn
Due on Match 18.