## Slide 1: Lecture 03: 80X86 Microprocessor

## Slide 2: Reference Book:
The 80x86 IBM PC and Compatible Computers
  Chapter 1 80X86 Microprocessor
  Chapter 9.1 8088 Microprocessor
微型计算机原理与接口技术（第四版）
  第2章 8086系统结构
  第3章 8086的寻址方式和指令系统

## Slide 3: Evolution of 80X86 Family
8086, born in 1978
  First 16-bit microprocessor
  20-bit address data bus, i.e. 220 = 1MB memroy
  First pipelined microprocessor
8088
  Data bus: 16-bit internal, 8-bit external
  Fit in the 8-bit world, e.g., motherboard, peripherals
  Adopted in the IBM PC + MS-DOS open system
80286, 80386, 80486
  Real/protected modes
  Virtual memory

## Slide 4: Internal Structure of 8086
Two sections
  Bus interface unit (BIU): accesses memory and peripherals
  Execution unit (EU): executes instructions previously fetched
  Work simultaneously

## Slide 5: Internal Structure of 8086

## Slide 6: Bus Interface Unit
Takes in charge of data transfer between CPU and memory as well as I/O devices
  Instruction fetch, instruction queuing, operand fetch and storage, address relocation and Bus control
Consists of :
  four 16-bit segment registers: CS, DS, ES, SS
  One 16-bit instruction pointer: IP
  One 20-bit address adder: e.g., CS left-shifted by 4 bits + IP (CS*16+IP)
  A 6-byte instruction queue
While the EU is executing an instruction, the BIU will fetch the next one or several instructions from the memory and put in the queue

## Slide 7: Execution Unit
Takes in charge of instruction execution
Consists of:
  Four 16-bit general registers: Accumulator (AX), Base (BX), Count (CX) and Data (DX)
  Two 16-bit pointer registers: Stack Pointer (SP), Base Pointer (BP)
  Two 16-bit index registers: Source Index (SI) and Destination Index (DI)
  One 16-bit flag register: 9 of the 16 bits are used
  ALU

## Slide 8: Registers
On-chip storage: super fast & expensive
Store information temporarily
Six groups

## Slide 9: Pipelining in 8086
BIU fetches and stores instructions once the queue has more than 2 empty bytes
EU consumes instructions pre-fetched and stored in the queue at the same time
Increases the efficiency of CPU
When does it work?
  Sequential instruction execution
  Branch penalty: when jump instruction executed, all pre-fetched instructions are discarded

## Slide 10: 8086/8088 Pins (Compare them and tell the difference)

## Slide 11: Minimum Mode Configuration
8086/88’s two work modes:
Minimum mode： =1
  Single CPU;
  Control signals from the CPU
Maximum mode： =0
  Multiple CPUs(8086+8087)
  8288 control chip supports

## Slide 12: Control Signals
MN/~MX: Minimum mode (high level), Maximum mode (low level)
~RD: output, CPU is reading from memory or IO
~WR: output, CPU is writing to memory or IO
M/~IO: output, CPU is accessing memory (high level) or IO (low level)
READY: input, memory/IO is ready for data transfer
~DEN: output, used to enable the data transceivers
DT/~R: output, used to inform the data transceivers the direction of data transfer, i.e., sending data (high level) or receiving data (low level)
~BHE: output, ~BHE=0, AD8-AD15 are used, ~BHE=1, AD8-AD15 are not in use
ALE: output, used as the latch enable signal of the address latch

## Slide 13: Control Signals
HOLD: input signal, hold the bus request
HLDA: output signal, hold request ack
INTR: input, interrupt request from 8259 interrupt controller, maskable by clearing the IF in the flag register
INTA: output, interrupt ack
NMI: input, non-maskable interrupt, CPU is interrupted after finishing the current instruction; cannot be masked by software
RESET: input signal, reset the CPU
  IP, DS, SS, ES and the instruction queue are cleared
  CS = FFFFH
  What is the address of the first instruction that the CPU will execute after reset?
Notes: H represents hexadecimal numbers

## Slide 14: Remember CMOS Gates?

## Slide 15: Memory/IO Control Signals

## Slide 16: Address/Data Demultiplexing & Address latching
Notes: Z represent the high-impedance state

## Slide 17: Data Bus Transceiver

## Slide 18: 8086/88 Bus Cycle (for data transfers)
At least 4 clock cycles
Notes: 8086读周期时序:
在8086读周期内,有关总线信号的变化如下:
M/IO在整个读周期保持有效,当进行存储器读操作时,M/IO为高电平;当进行I/O端口读操作时,M/IO为低电平.
A19/S6～A16/S3是在T1期间,输出CPU要读取的存储单元的地址高4位.T2～T4期间输出状态信息S6～S3.
BHE/S7在T1期间输出BHE有效信号(BHE为低电平),表示高8位数据总线上的信息可以使用,BHE信号通常作为奇地址存储体的选择信号(偶地址存储体的选择信号是最低地址位A0).T2～T4期间输出高电平.
ADl5～AD0在T1期间输出CPU要读取的存储单元或I/O端口的地址A15～A0.T2期间为高阻态,T3～T4期间,存储单元或I/O端口将数据送上数据总线.CPU从ADl5～AD0上接收数据.
ALE:在T1期间地址锁存有效信号,为一正脉冲,系统中的地址锁存器正是利用该脉冲的下降沿来锁存A19/S6～A16/S3,ADl5～AD0中的20位地址信息以及BHE.
RD在T2期间输出低电平,送到被选中的存储器或I/O接口.要注意的是,只有被地址信号选中的存储单元或I/O端口,才会被RD信号从中读出数据(数据送上数据总线ADl5～AD0).
DT/R在整个总线周期内保持低电平,表示本总线周期为读周期.在接有数据总线收发器的系统中,用来控制数据传输的方向.
DEN在T2～T3期间输出有效低电平,表示数据有效.在接有数据总线收发器的系统中,用来实现数据的选通.
8086写周期时序总线写操作的时序与读操作时序相似,其不同处在于:
AD15～AD0在T2～T4期间送上欲输出的数据,而无高阻态.
WR在T2～T4期间输出有效低电平,该信号送到所有的存储器和I/O接口.要注意的是,只有被地址信号选中的存储单元或I/O端口才会被WR信号写入数据.
DT/R在整个总线周期内保持高电平,表示本总线周期为写周期.在接有数据总线收发器的系统中,用来控制数据传输方向.

## Slide 19: 8086 Programming
A typical program on 8086 consists of at least three segments
  code segment: contains instructions that accomplish certain tasks
  data segment: stores information to be processed
  stack segment: store information temporarily
What is a segment?
  A memory block includes up to 64KB. Why?
  Begins on an address evenly divisible by 16, i.e., an address looks like in XXXX0H. Why?

## Slide 20: Logical & Physical Address
Physical address
  20-bit address that is actually put on the address bus
  A range of 1MB from 00000H to FFFFFH
  Actual physical location in memory
Logical address
  Consists of a segment value (determines the beginning of a segment) and an offset address (a relative location within a 64KB segment)
  E.g., an instruction in the code segment has a logical address in the form of CS (code segment register):IP (instruction pointer)

## Slide 21: Logical & Physical Address
logical address -> physical address
  Shift the segment value left one hex digit (or 4 bits)
  Then adding the above value to the offset address
  One logical -> only one physical
Segment range representation
  Maximum 64KB
  logical 2500:0000 – 2500:FFFF
  Physical 25000H – 34FFFH (25000 + FFFF)

## Slide 22: Physical Address Wrap-around
When adding the offset to the shifted segment value results in an address beyond the maximum value FFFFFH
E.g., what is the range of physical addresses if CS=FF59H?
  Solution:
  The low range is FF590H, and
  the range goes to FFFFFH and
  wraps around from 00000H to
  0F58FH (FF590+FFFF).

## Slide 23: Logical & Physical Address
Physical address -> logical address ?
  One physical address can be derived from different logical addresses
  E.g.,

## Slide 24: Segment Overlapping
Two segments can overlap
  Dynamic behaviour of the segment and offset concept
  May be desirable in some circumstances

## Slide 25: Code Segment
8086 fetches instructions from the code segment
  Logical address of an instruction: CS:IP
  Physical address is generated to retrieve this instruction from memory
  What if desired instructions are physically located beyond the current code segment?
  Solution: Change the CS value so that those instructions can be located using new logical addresses

## Slide 26: Data Segment
Information to be processed is stored in the data segment
  Logical address of a piece of data: DS:offset
    Offset value: e.g., 0000H, 23FFH
    Offset registers for data segment: BX, SI and DI
  Physical address is generated to retrieve data (8-bit or 16-bit) from memory
  What if desired data are physically located beyond the current data segment?
  Solution: Change the DS value so that those data can be located using new logical addresses

## Slide 27: Data Representation in Memory
Memory can be logically imagine as a consecutive block of bytes
How to store data whose size is larger than a byte?
  Little endian: the low byte of the data goes to the low memory location
  Big endian: the high byte of the data goes to the low memory location
  E.g., 2738H

## Slide 28: Stack Segment
A section of RAM memory used by the CPU to store information temporarily
  Logical address of a piece of data: SS:SP (special applications with BP)
  Most registers (except segment registers and SP) inside the CPU can be stored in the stack and brought back into the CPU from the stack using push and pop, respectively
  Grows downward from upper addresses to lower addresses in the memory allocated for a program
    Why? To protect other programs from destruction
    Note: Ensure that the code section and stack section would not write over each other

## Slide 29: Push & Pop
16-bit operation
Little endian or big endian?

## Slide 30: Push & Pop

## Slide 31: Extra Segment
An extra data segment, essential for string operations
  Logical address of a piece of data: ES:offset
    Offset value: e.g., 0000H, 23FFH
    Offset registers for data segment: BX, SI and DI
In Summary,

## Slide 32: Memory map of the IBM PC
1MB logical address space
640K max RAM
  In 1980s, 64kB-256KB
  MS-DOS, application software
  DOS does memory management; you do not set CS, DS and SS
Video display RAM
ROM
  64KB BIOS
  Various adapter cards
Notes: It seems that all address space is assigned to only memory. So what about I/O devices?

## Slide 33: BIOS Function
Basic input-output system (BIOS)
  Tests all devices connected to the PC when powered on and reports errors if any
  Load DOS from disk into RAM
  Hand over control of the PC to DOS
Recall that after CPU being reset, what is the first instruction that CPU will execute?

## Slide 34: Flag Register
16-bit, status register, processor status word (PSW)
6 conditional flags
  CF, PF, AF, ZF, SF, and OF
3 control flags
  DF, IF, TF

## Slide 35: Conditional Flags
CF (Carry Flag): set whenever there is a carry out, from d7 after a 8-bit op, from d15 after a 16-bit op
PF (Parity Flag): the parity of the op result’s low-order byte, set when the byte has an even number of 1s
AF (Auxiliary Carry Flag): set if there is a carry from d3 to d4, used by BCD-related arithmetic
ZF (Zero Flag): set when the result is zero
SF (Sign Flag): copied from the sign bit (the most significant bit) after op
OF (Overflow Flag): set when the result of a signed number operation is too large, causing the sign bit error

## Slide 36: More about Signed Number, CF&OF
The most significant bit (MSB) as sign bit, the rest of bits as magnitude
  For negative numbers, D7 is 1, but the magnitude is represented in 2’s complement
CF is used to detect errors in unsigned arithmetic operations
OF is used to detect errors in signed arithmetic operations
  E.g., for 8-bit ops, OF is set when there is a carry from d6 to d7 or from d7 out, but not both

## Slide 37: Examples of Conditional Flags
OF = 0 since there is no carry from d6 to d7 and no carry beyond d7
How can CPU know whether an operation is unsigned or signed?
Notes: In CPU, we have an adder circuitry but no subtractor circuitry so when doing subtraction x-y, we add x to the 2’s complement of y.
What’s 2’s complement of a binary number? Invert all bits and then add 1 to the result.

## Slide 38: Control Flags
IF (Interrupt Flag): set or cleared to enable or disable only the external maskable interrupt requests
  After reset, all flags are cleared which means you (as a programmer) have to set IF in your program if allow INTR.
DF (Direction Flag): indicates the direction of string operations
TF (Trap Flag): when set it allows the program to single-step, meaning to execute one instruction at a time for debugging purposes

## Slide 39: 80X86 Addressing Modes
How CPU can access operands (data)
80X86 has seven distinct addressing modes
  Register
  Immediate
  Direct
  Register indirect
  Based relative
  Indexed relative
  Based indexed relative
Take the MOV instruction for example
  MOV destination, source
  Destination and source should have the same size

## Slide 40: Register Addressing Mode 寄存器寻址方式
Data are held within registers
  No need to access memory
  E.g.,
Data can be moved among ALL registers except CS, IP

## Slide 41: Immediate Addressing Mode 直接寻址方式
The source operand is a constant
  Embedded in instructions
  No need to access memory
  E.g.,
Immediate numbers CANNOT be moved to segment registers
How to change the value of a segment register?

## Slide 42: Direct Addressing Mode 直接寻址方式
Data is stored in memory and the address is given in instructions
  Offset address in the data segment (DS) by default
  Need to access memory to gain the data
  E.g.,

## Slide 44: Register Indirect Addressing Mode 寄存器间接寻址方式
Data is stored in memory and the address is held by a register
  Offset address in the data segment (DS) by default
  Registers for this purpose are SI, DI, and BX
  Need to access memory to gain the data
  E.g.,

## Slide 46: Based Relative Addressing Mode
Data is stored in memory and the address can be calculated with base registers BX and BP as well as a displacement value
  The default segment is data segment (DS) for BX, stack segment (SS) for BP
  Need to access memory to gain the data
  E.g.,

## Slide 48: Indexed Relative Addressing Mode
Data is stored in memory and the address can be calculated with index registers DI and SI as well as a displacement value
  The default segment is data segment (DS)
  Need to access memory to gain the data
  E.g.,

## Slide 50: Based Indexed Relative Addressing Mode
Combines based and indexed addressing modes, one base register and one index register are used
  The default segment is data segment (DS) for BX, stack segment (SS) for BP
  Need to access memory to gain the data
  E.g.,

## Slide 52: Segment Overrides
Offset registers are used with default segment registers
80X86 allows the program to override the default segment registers
  Specify the segment register in the code

## Slide 53: Assignment Three
Go Canvas site and download the Assignment Three
  https://oc.sjtu.edu.cn