## Slide 1: Lecture 04: Assembly Language Programming (1)

## Slide 2: Reference Book:
The 80x86 IBM PC and Compatible Computers
  Chapter 2 Assembly Language Programming
微型计算机原理与接口技术（第四版）
  第3章 8086的寻址方式和指令系统
  第4章 汇编语言程序设计

## Slide 3: Programming Languages
Machine language
  Binary code, for CPU but not human beings
Assembly language
  Mnemonics for machine code instructions
  Low-level language: deals with the internal structure of a CPU
  Hard to program, poor portability but very efficient
BASIC, Pascal, C, Fortran, Perl, TCL, Python, …
  High-level languages: do not have to be concerned with the internal details of a CPU
  Easy to program, good portability but less efficient
How to convert your program in low/high-level languages into machine language?

## Slide 4: Assembly Language Programs
A series of statements
  Assembly language instructions
    Perform the real work of the program
  Directives (pseudo-instructions)
    Give instructions for the assembler program about how to translate the program into machine code.
Consists of multiple segments
  But CPU can access only one data segment, one code segment, one stack segment and one extra segment (Why? )

## Slide 5: Form of an statement
[label:] mnemonic [operands] [;comment]
  label is a reference to this statement
    Rules for names: each label must be unique; letters, 0-9, (?), (.), (@), (_), and ($); first character cannot be a digit; less than 31 characters
  “:” is needed if it is an instruction otherwise omitted
  “;” leads a comment, the assembler omits anything on this line following a semicolon

## Slide 6: Shell of a Real Program
Full segment definition (old fashion)
  See an example later
Simplified segment definition

## Slide 7: Model Definition
The MODEL directive
  Selects the size of the memory model
  SMALL: code <=64KB, data <=64KB
  MEDIUM: data <=64KB, code >64KB
  COMPACT: code<=64KB, data >64KB
  LARGE: data>64KB but single set of data<64KB, code>64KB
  HUGE: data>64KB, code>64KB
  TINY: code + data<64KB

## Slide 8: Simplified Segment Definition
Simplified segment definition
  .CODE, .DATA, .STACK
  Only three segments can be defined
  Automatically correspond to the CPU’s CS, DS, SS
  DOS determines the CS and SS segment registers automatically. DS (and ES) has to be manually specified.

## Slide 9: Segments All at a Glance
Stack segment
Data segment
  Data definition
Code segment
  Write your statements
  Procedures definition
    label PROC [FAR|NEAR]
    label ENDP
  Entrance proc should be FAR

## Slide 10: Full Segment Definition
Full segment definition
  label SEGMENT
  label ENDS
  You name those labels
  as many as needed
  DOS assigns CS, SS
  Program assigns DS (manually load data segments) and ES

## Slide 11: Program Execution
Program starts from the entrance
  Ends whenever calls 21H interruption with AH = 4CH
Procedure caller and callee
  CALL procedure
  RET

## Slide 12: Build up Your Program

## Slide 13: Control Transfer Instructions
Range
  SHORT, intrasegment
    IP changed: one-byte range (-128~127)
  Near, intrasegment
    IP changed: two-bytes range (-32768~32767)
    If control is transferred within the same code segment
  FAR, intersegment
    CS and IP all changed
    If control is transferred outside the current code segment
Jumps
CALL statement

## Slide 14: Conditional Jumps
Jump according to the value of the flag register
Short jumps

## Slide 15: Unconditional Jumps
JMP [SHORT|NEAR|FAR PTR] label
Near by default

## Slide 16: Subroutines & CALL Statement
Range
  NEAR: procedure is defined within the same code segment with the caller
  FAR: procedure is defined outside the current code segment of the caller
PROC & ENDP are used to define a subroutine
CALL is used to call a subroutine
  RET is put at the end of a subroutine
  Difference between a far and a near call?

## Slide 19: Data Types & Definition
CPU can process either 8-bit or 16 bit ops
  What if your data is bigger?
Directives
  ORG: indicates the beginning of the offset address
    E.g., ORG 10H
  Define variables:
    DB: allocate byte-size chunks
      E.g., x DB 12 | y DB 23H,48H | Z DB ‘Good Morning!’ | str DB “I’m good!”
    DW, DD, DQ
  EQU: define a constant
    E.g., NUM EQU 234
  DUP: duplicate a given number of characters
    E.g., x DB 6 DUP(23H) | y DW 3 DUP(0FF10H)

## Slide 20: More about Variables
For variables, they may have names
  E.g., luckyNum DB 27H, time DW 0FFFFH
Variable names have three attributes:
  Segment value
  Offset address
  Type: how a variable can be accessed (e.g., DB is byte-wise, DW is word-wise)
Get the segment value of a variable
  Use SEG directive (E.g., MOV AX, SEG luchyNum)
Get the offset address of a variable
  Use OFFSET directive, or LEA instruction
  E.g., MOV AX, OFFSET time, or LEA AX, time
Logical address

## Slide 21: More about Labels
Label definition:
  Implicitly:
    E.g., AGAIN: ADD AX, 03423H
  Use LABEL directive:
    E.g., AGAIN LABEL FAR
    ADD AX, 03423H
Labels have three attributes:
  Segment value:
  Offset address:
  Type: range for jumps, NEAR, FAR
Logical address

## Slide 22: More about the PTR Directive
Temporarily change the type (range) attribute of a variable (label)
  To guarantee that both operands in an instruction match
  To guarantee that the jump can reach a label
E.g., DATA1 DB 10H,20H,30H ;
DATA2 DW 4023H,0A845H
……
MOV BX, WORD PTR DATA1 ; 2010H -> BX
MOV AL, BYTE PTR DATA2 ; 23H -> AL
MOV WORD PTR [BX], 10H ; [BX],[BX+1]←0010H
E.g., JMP FAR PTR aLabel

## Slide 23: .COM Executable
One segment in total
  Put data and code all together
  Less than 64KB